## Slide 1: Auto ReTest Function
HT-9xxx Series
RD5
Steven Chou
2017.01.26
Rework @ 2022.05.13

## Slide 2
01
02
Introduce of ART
Tray Arm
Conveyor Track
Hardware Modification
04
GS32 Bin Test Mode
ART Test Command and Flow
Communication Flow
03
ART GUI
BIN Setting
Software Function

## Slide 3: Introduce of ART
Lot in
Normal test
Print summary
RT lot in
Retest
Print summary
Originally, operator doing RT lot in and print summary manually.
In ART function, handler swap the test mode and tell tester to print summary AUTOMATICALLY.
A
R
T

## Slide 4: Hardware Modification
Tray Arm
Change to chuck type.
Add cover.
Conveyor Track
Must be 6 auto track.
All conveyor can move tray in and out.
Separator of unloader use cylinder.

## Slide 5: Software Function
[A10] Auto retest parameter
Enabled function [A10-1] to use ART function.
[A10-3] can lock the test mode to specify protocol.

## Slide 6: Software Function
Main GUI
Additional panel for ART information.
Add ‘Initial ART’ in running mode.

## Slide 7: Software Function
Check QTY
QTY provide by tester.
Lot number provided by tester.
Maximum RT count.
Current RT count.
No RT bin yield to stop ART.
Current yield for ART pass category.
Device count which place to unloader.
Device count which need to RT
Devices count which need to load.
Devices count which pick up from loader.
Devices count which place to in shuttle.
Device count for each auto unloader which need to RT.

## Slide 8: Software Function
Check QTY
Gap counts devices count which happened error.
The error include:
In arm pick error on hot plate with skip action.
In arm drop error with skip action.
Gap counts devices count which happened error.
The error include:
Index pick up error on shuttle with skip action.
Index device drop error with skip action.
Device lose at out shuttle.
Out arm pick error on hot plate with skip action.
Out arm drop error with skip action.

## Slide 9: Software Function
Active setting panel for ART.

## Slide 10: Software Function
Level Set for ART Setting Panel
Priority of ART setting panel
Control by [130] Yield – ART Setting
Control by [129] Yield – ART User Fix

## Slide 11: Software Function
ART Lot Info
Modify for input quantity by engineer.
Modify for handler status by engineer.
Modify for RT try count.
Modify for pass rate.

## Slide 12: Software Function
ART Additional Setting
Sort mode include: Assigned Category and Category R.
RT start mode can choose :
Auto progress : change status automatically.
Manual progress : alarm and wait user to start.
Handler will turn off the DUT when running RT. And can set the rule to close site.
When handler have such status, user can decides to alarm or auto change handler status to next step.
When in arm pick up error, it can auto skip to next device.

## Slide 13: Software Function
Assigned Category
In this case, only the bin setting on Auto 2 will do retest.
In ART mode, we will use bin setting as
  ART-Normal for FT and RT;
  ART-Retest bin setting for final RT.

## Slide 14: Software Function
Category R
In this case, Auto 2, Fix 1, Fix 2 and Fix 3 will combine bin to Auto 2 when FT and RT.
And will separate bin in final RT
You can set bin combine to bin R when FT and RT to one unloader.
And it will be separate to define bin in final RT.

## Slide 15: Software Function
Auto Socket Off
Socket can be turn off when RT and turn on in FT.
Function | Description
Auto Head | Compare to the head has best yield, if lower than setting rate, the site by such head will be close.
Auto Socket | Compare to the socket has best yield, if lower than setting rate, the site will be close.
Manual | User can select which head or site to close.

## Slide 16: Software Function
Correction QTY
You can use the user fix tool to correction the quantity when number is not match.
Input count need to RT.
Input count NO need to RT.
Output count need to RT.
Output count NO need to RT.

## Slide 17: Software Function
Correction QTY
You can try the formula in excel to know how correction works.

## Slide 18: Communication Flow
New GPIB Bin Type
We add 16 bin GS and 32 bin GS in GPIB test type. You can change mode in Test IF panel.

## Slide 19: Communication Flow
New Test Mode
The bin mapping and BINON command of General Type, 16 bin GS and 32 bin GS are as the table below.
Mode | GPIB BINON command
General | BINON:00000000,00000000,00000000,FEDC4321;
16 Bin GS | BINON:A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,G,F,E,D,4,3,2,1;
32 Bin GS | BINON:A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,A,10,F,E,D,4,3,2,1;

## Slide 20: Communication Flow
General Flow of ART
Handler
Tester
Initial Lot
Lot Info
FT Lot End
Request FT lot End
Print Summary
RT Start
Auto Move RT Tray to Loader
Doing FT test
RT Lot End
Doing RT test
Need RT?
Request Final Lot End
Print Summary
Lot End
Yes
No

## Slide 21: Communication Flow
Initial Tester Connection of ART
Handler
Tester
Tester Connect
FR?
FR0
DL 0
Go to Lot Information
SRQMASK FF

## Slide 22: Communication Flow
Initial Lot Information of ART
Handler
Tester
Initial Lot
LOTCLEAR?
LOTCLEARED
INPUTQTY NN,XX
Go to FT Lot Start
SETTINGOK / SETTINGNG
Got SETTINGOK?
Yes
No
NN : Lot IC count.
XX : Lot ID

## Slide 23: Communication Flow
FT Lot Start
Handler
Tester
FT Lot Start
SRQKIND?
SRQ 0xC0
LOTORDER 0
Go to Lot End Flow
SRQKIND 2
Testing
Tester is ready for testing.
2 : First time lot start

## Slide 24: Communication Flow
Lot End
Handler
Tester
Lot End
SRQKIND?
SRQ 0xC0
LOTRETESTCLEAR?
Go to RT Lot Start
SRQKIND 8
Need RT?
Go to Final Lot End
Yes
No
LOTRETESTCLEARED
LOTORDER 2
Auto Move RT Tray to Loader
8 : FT / RT lot end.
2 : Print summary.

## Slide 25: Communication Flow
RT Lot Start
Handler
Tester
RT Lot Start
SRQKIND?
SRQ 0xC0
LOTORDER 0
Go to Lot End Flow
SRQKIND 4
Testing
Tester is ready for testing.
4 : RT lot start

## Slide 26: Communication Flow
Final Lot End
Handler
Tester
Final Lot End
SRQKIND?
SRQ 0xC0
LOTORDER 2
SRQKIND 10
Tray Feed and End of ART Flow
2 : Print summary.
10 : Final RT lot end

## Slide 27: Communication Flow
Command List of ART
Tester Command | Description | Reply by Handler
LOTCLEAR? | Request to clear lot data on handler. | LOTCLEARED : all lot data is cleared. SETTINGNG : can not cleat lot data.
INPUTQTY NN,XX | Set lot quantity to handler. NN is count of IC in lot. XX is Lot ID. | SETTINGOK : nothing error. SETTINGNG : can not set lot data.
SRQKIND ? | Asking handler for running status. | SRQKIND 2 : FT lot start. SRQKIND 4 : RT lot start. SRQKIND 8 : lot end. SRQKIND 10 : final lot end.
LOTORDER X | By the SRQKIND command, tester will reply LOTORDER. | LOTORDER 0 : handler can start running. LORORDER 2 : Reply to perform ART or clean out lot end.
LOTRETESTCLEAR? | Request to clear lot data on handler. | LOTRETESTCLEARED: all lot data is cleared. SETTINGNG : can not cleat lot data.

## Slide 28: Thank you